## Slide 1
GRASSROOTS NETWORKING · STUDENT PROJECT
NAT Topology and Hole-Punching Survey
Grassroots approach to classifying NATs
Dan Bachar · dan.bachar@campus.technion.ac.il

## Slide 2
WHO CAN FACILITATE
Well-connected devices
Register address with a well-connected friend
→
Ask it for the other peer’s address
→
It tells both sides to punch at once
→
The peers talk directly
Well-connected: has a public address, so anyone can reach it.
It facilitates between mutual friends by passing on addresses, as well as coordinating punching.
Today simple private address regex decides who qualifies: we replace it with an algorithmic test.

## Slide 3
WHAT WE MUST DISTINGUISH
NAT behavior
BEHAVIOR
EXAMPLE
EFFECT ON HOLE PUNCHING
AUTONAT
REACHABILITY
Endpoint-independent
formerly: cone
home routers
One external port for every destination. Punching works.
EndpointIndependent
Public if filtering is open, else Private
Address-dependent
formerly: no name
enterprise NATs
A new port per destination address. Both sides must punch.
EndpointDependent
Private
Address-and-port-dependent
formerly: symmetric
mobile carriers
A new port per endpoint. Punching fails without prediction.
EndpointDependent
Private
Carrier-grade NAT
mobile carriers
Sits on top of the others. Nothing unsolicited gets in.
no name
Private
We measure four properties:
1. Mapping: which external port the NAT assigns.
2. Filtering: which senders it lets in.
3. Port preservation: whether it keeps our own port.
4. Lifetime: how long it keeps an idle mapping.
AutoNAT also reports reachability (Public, Private or Unknown)

## Slide 4
AN ADDRESS RANGE TEST
Self-classification
not 10.* | 192.168.* | ...
Well-connected if the advertised address is in none of the private or reserved ranges.
A phone behind carrier NAT passes it
It advertises the carrier’s public address, so it looks reachable.
Hole punching is skipped despite CGNAT not allowing unsolicited incoming requests.
Peer is considered well-connected, although nobody can reach it.
A public address does not mean peer can be reached.

## Slide 5
THE ALGORITHM
Witness-based detection
1
Pick A, a well-connected friend we have a link to; B, a linked friend; C, a friend of A with no link to us.
2
A and B report the address and port they see us at.
3
Ask A to start a punch between us and C. A gives C our address as A saw it. We send nothing.
4
C’s punch packets, carrying its key, arrive: anyone can reach us. Not after retries: filtering is endpoint-dependent.
5
A and B saw one port: mapping is endpoint-independent. Two ports: endpoint-dependent.
Probe
the phone under test
Friend A
linked, well-connected; reports, signals
Friend B
linked, another address; reports
Friend C
no link; punches toward us

## Slide 6
TWO ROUNDS
The procedure
Dial back
filtering: A tells C to punch toward us; we send nothing
C’s packets arrive: anyone can reach us
endpoint-independent
They do not, after retries via more friends
endpoint-dependent
A’s packet always arrives; it proves only the link
no verdict
Reflect
mapping: A and B report the port they saw us at
Both saw the same port
endpoint-independent
They saw different ports
endpoint-dependent
Address- or port-dependent? One source per friend cannot tell
oracle only
Friends separate independent from dependent, the split autoNAT reports. The finer split needs the oracle.

## Slide 7
A FALSE YES AND A FALSE NO
Two things that mislead
False yes: contamination
If we ever sent to C, our packets opened the hole.
The normal punch sends from both sides. We send nothing.
Guard: log where we sent; ignore punches from there.
False no: loss
Arrival is proof. Absence is not: the packet may be lost.
Or C was offline, or A did not pass the request on.
Retry, then ask A for another C, before recording no.

## Slide 8
WHAT WE MEASURE, AND FROM WHERE
Testbed and hosting
What we measure
Our own smartphones, on carrier and home paths.
A group: one carrier, one kind of plan.
Two SIMs and Android plus iOS per carrier.
What the institution hosts
Oracle: a reference NAT-test server.
Witnesses: small hosts, different networks.
Bench: fake NATs built on one Linux machine.